VL-H05

Feature

- 1/4" 1.0 Megapixel CMOS Sensor，Max image Resolution 1280*720@25fps

- H.264 Main Profile @ level 3.0 coding, Real time H.264 dual-stream encoding, resolution, frame rate, bit rate adjustable

- Support Color/BW mode converting, IR-CUT Filter

- Build in Motion Detection,

- Support Plug-and-Play, including PC surveillance platform and mobile client, Easy to remote

- Integrated ONVIF standard, Compatibility with third-party ONVIF platform software

- IP66 Rated Waterproof, Outdoor use

Specifications

| Model | VL-H05 |
| --- | --- |
| Hardware |
| Processor | HI3518C |
| Sensor | 1/4" 1.0 Megapixel CMOS Sensor |
| Lens | 4mm lens |
| IR LED | 32 IR LEDs, IR Distance 10~20M |
| Day/Night | IR-CUT |
| Min. Illumination | 0.5lux; 0 lux with IR on |
| Max S/N Ratio | 50dB |
| Video |
| Compression | H.264 |
| image | main stream: 1280x720@1-25fps sub stream: 640x360@1-25fps 320x180@1-25fps |
| Bit Rate | 128~4096kbps, Supports CBR/VBR |
| Image Control | Hue, saturation, brightness, contrast, exposure |
| Auto Image Control | AE, AWB |
| Audio |
| Compression | G.711-A |
| Bit Rate | 64kbps/128kbps |
| Talkback | support |
| Network |
| Protocol | TCP/IP, HTTP, DHCP, DNS, DDNS, RTP, RTSP, PPPoE, SMTP, NTP, SNMP, FTP, UPNP |
| Compliance | ONVIF 2.1(1.02 backward compatible) |
| PC Client and Browser | ISS, IE6.0 and above |
| Mobile phone | Iphone, ipad, Android |
| WIFI Encryption | WAP, WAP2 |
| LAN | 1 RJ45 10M/100M Ethernet port |
| General |
| Working Temperature | -10℃~ +55℃ |
| Working Humidity | 0% - 90% |
| Protection Level | IP66 Rated Waterproof |
| Power Supply | DC 12 V/1A |
| Power Consumption | Maximum 6w |
| Dimensions | 50*45*150mm |
| Weight | 1.0kg |
| Approvals | CE , FCC, RoHS |